The Kalman Filter:

A system with state vector xt evolves according to:
xt = Atxt-1 + Btut + wt (1)
here
xt is the state vector at time t
At is the prediction matrix; it captures the system’s dynamics
ut is a control input signal
Bt is the control matrix; it describes how the control input affects the system
wt is some random noise with an associated covariance matrix Qt
Equation (1) specifies how the system’s true state xt evolves from one time step to the next.
We want to find the best estimate x̂t of xt at time t, based on x̂t-1. (Note that the true xt and wt are unknown to the estimator.)
Here is the update equation for x̂t :
x̂t = Atx̂t-1 + Btut (2)
Pretty straightforward. wt doesn’t enter into it because it is assumed to be symmetrically distributed around the null vector and independent of xt .
We also want to update the uncertainty in our best estimate x̂t , i.e. the covariance matrix Pt associated with x̂t , from one time step to the next.
Pt is the matrix of variances and covariances between elements of x̂t . Its elements are Pij = σij2 , which may be expressed as
Pt = E[(xt - x̂t)(xt - x̂t)T] (3)

Substituting equations (1) and (2) into (3) we can derive the update formula for Pt:
Pt = E[(xt - x̂t)(xt – x̂t)T]	1
    = E[((Axt-1 + But +wt) – (Ax̂t-1 + But))) ((Axt-1 + But +wt) – (Ax̂t-1 + But))T ] 2
    = E[(A(xt-1 – x̂t-1) + wt) (A(xt-1 – x̂t-1) + wt)T]	3
    = E[(A(xt-1 – x̂t-1)) (A(xt-1 – x̂t-1))T] + E[wtwtT]	4
    = E[(A(xt-1 – x̂t-1)) ((xt-1 – x̂t-1)TAT)] + E[wtwtT]	5
    = AE[(xt-1 – x̂t-1) (xt-1 – x̂t-1)T]AT + E[wtwtT]	6
    = APt-1AT + Qt	7

In line 4, we have dropped terms like E[A(xt-1 – x̂t-1)wt]; they are zero because the x and w processes are independent. In line 5, we used the matrix algebra rule
(AB)T = BTAT, in this case (A(xt-1 – x̂t-1) )T= (xt-1 – x̂t-1)TAT. And in line 6 we moved the E inside the A operation; this is ok because A is constant.
So the update rule for the covariance matrix Pt associated with our best estimate x̂t is
Pt = APt-1AT + Qt	(4)

Next, we add some measurements. The measurements are produced by sensors operating on the actual state xt, and they produce a vector of measurements µt. We model the sensors with a matrix Ht:
é èê μ ^^ μ

µt= Ht x̂t	(5)